## Slide 1
NetSage AI: AI Deployment & Automation
For Cisco Network Troubleshooting
DEGREE & DEPARTMENT
B.Tech (CSE) — School of Computer Science & Engineering
CANDIDATE INFORMATION
FACULTY MENTOR
Prof. Swati Vashisht
Instructor, IILM University & Cisco Networking Academy
IILM UNIVERSITY
Greater Noida, Uttar Pradesh
Mohammad Amaan Aslam
ROLL NUMBER
2410030089
ACADEMIC BATCH
2026–2027

## Slide 2
Student Profile
Project Verification
STUDENT NAME
Mohammad Amaan Aslam
ROLL NUMBER
2410030089
DEGREE PROGRAM
Bachelor of Technology (B.Tech) in CSE
ACADEMIC SESSION
2026–2027 Batch
INSTITUTION
IILM University, Greater Noida, U.P.
PROJECT TITLE
NetSage AI: AI Deployment & Automation for Cisco Network Troubleshooting
SPONSORING PLATFORM
Cisco Networking Academy Virtual Internship
FACULTY SUPERVISOR
Prof. Swati Vashisht
DECLARATION SCOPE
Original work completed in partial fulfillment of B.Tech (CSE) degree
Candidate Declaration & Academic Details

## Slide 3
Global Technical Skill Leader: Cisco Networking Academy provides structured IT, networking, cybersecurity, and modern AI curricula worldwide.
Academic Partnership with IILM: Direct collaboration providing hands-on lab environments and virtual internship projects to engineering undergraduates.
Emerging AI & Automation Domain: Focuses on integrating modern AI frameworks with network telemetry, CLI diagnostics, and deterministic modeling.
Industry Standard Tools: Hands-on training utilizing Cisco Packet Tracer, Cisco IOS CLI, Python automation scripts, and LLM prompt engineering.
Sponsoring Organization: Cisco Networking Academy

## Slide 4
Root-Cause Isolation Challenge
Junior network engineers frequently know isolated CLI commands but struggle to connect symptoms to exact root causes in multi-layer network environments (L1 to L7).
When a host gets an IP but cannot reach a server, pinpointing whether the failure stems from VLAN tagging, gateway mismatches, DHCP relay drops, ACL blocks, or NAT pool exhaustion is time-consuming.
Operational Risk of Unchecked AI
Fully autonomous AI models present severe enterprise risks if permitted to execute unverified CLI changes directly on production network infrastructure.
NetSage AI resolves this by coupling structured AI recommendations with mandatory human-in-the-loop review and deterministic pre-validation.
Problem Statement: Multi-Layer Diagnostic Friction

## Slide 5
1. Scenario Dataset Construction
Build 30 real-world Cisco Packet Tracer lab cases representing complex Layer 1 through Layer 7 network failure scenarios.
2. Deterministic Rule Checker
Develop Python script (`rule_checker.py`) to parse CLI text and immediately flag L1-L3 configuration errors prior to AI inference.
3. Strict JSON Prompt Templates
Design prompt templates forcing LLMs to return strict JSON schema containing root cause, confidence score, CLI evidence, and fix steps.
4. Responsible AI Audit Logging
Maintain an audit log recording human review decisions (Accept, Edit, Reject) to enforce safety and prevent erroneous CLI changes.
Core Project Objectives & Pillars

## Slide 6
End-to-End AI Deployment Pipeline: From multi-layer Cisco lab case synthesis to deterministic Python rule checks, prompt engineering, and executive dashboards.
Layer 2 & Switching Protocols: 802.1Q trunking, VLAN tagging, Spanning Tree Protocol (STP), EtherChannel link aggregation, and port security.
Layer 3 & Routing Protocols: Static routes, RIPv2, OSPF, EIGRP, HSRP gateway redundancy, and Subnetting / IP allocation.
Layer 4-7 Services & Security: Dynamic NAT/PAT, Standard & Extended ACLs, DHCP Relays, DNS/Web server reachability, and Wireless/RADIUS.
Technical Scope & Protocol Coverage

## Slide 7
1. Input Data Layer
Captures Packet Tracer symptoms, topology notes, and CLI `show` command outputs (`show run`, `show ip int brief`, `show ip route`).
2. Deterministic Rule Checker
Python script (`rule_checker.py`) uses regular expressions to catch shutdown interfaces, duplicate IPs, and mismatched timers instantly.
3. AI Prompt Engine
Routes unflagged symptoms to prompt templates, enforcing strict JSON schema output with quoted evidence and verification commands.
4. Human Review Dashboard Layer
Presents AI findings to a human engineer with options to Accept, Edit, or Reject the recommended fix.
5. Audit & Execution Layer
Logs all decisions into the Responsible AI Audit Log and pushes human-approved CLI commands to network devices.
NetSage AI 5-Layer System Architecture

## Slide 8
Simulation & CLI
Cisco Packet Tracer 8.x: Network environment simulation. Cisco IOS CLI: Command execution & output capture.
Programming & Automation
Python 3.8+: `rule_checker.py` script. Pandas & Regex: Log parsing & output validation.
AI & LLM Architectures
Gemini & ChatGPT: Generative AI inference. JSON Schema: Structured few-shot prompt templates.
Dashboard & Audit
Microsoft Excel: KPI blocks & pivot charts. Responsible AI Log: Human override record keeping.
Technologies & Technical Toolchain

## Slide 9
Data Collection
Synthesized 30 Cisco Packet Tracer lab cases spanning L1–L7 fault scenarios.
Prompt Setup
Engineered few-shot templates enforcing strict JSON schema responses.
Rule Checker
Built `rule_checker.py` script to instantly capture basic L1-L3 errors.
AI Diagnosis
Executed AI inference and compared diagnostic output against ground truth.
Human Audit
Evaluated every AI diagnosis through mandatory human reviewer oversight.
Dashboarding
Aggregated agreement metrics into Executive Excel KPI Dashboards.
6-Step Project Execution Methodology

## Slide 10
Across 30 test cases, NetSage AI achieved an 83.3% initial agreement rate with human experts. The Python deterministic script flagged 10 basic cases before AI execution, saving inference time.
Quantitative Evaluation: Case Breakdown

## Slide 11
The high agreement rate demonstrates robust prompt formatting, while the 16.7% edited/rejected subset highlights the necessity of human oversight in preventing bad CLI commands from executing.
Human Oversight & Agreement Distribution

## Slide 12
Case ID | Reported Network Symptom | Decision | Corrected Root Cause & Technical Audit
NET-005 | Web page won't load; public IP ping works. | Rejected | Incorrect DNS server IP configured on client PC (192.168.1.250). AI missed client-side DNS setting.
NET-007 | Guest Wi-Fi reaches corporate server. | Rejected | ACL BLOCK_GUEST permits traffic & not bound to subinterface. AI suggested wrong ACL direction.
NET-013 | SSH access denied from admin station. | Edited | VTY ACL 10 restricts access to wrong host (.10 instead of .50). Human corrected host IP mask.
NET-020 | HSRP fails to pre-empt back to R1. | Edited | Missing `standby 1 preempt` command on R1. AI identified priority drop but missed preemption rule.
NET-027 | Dynamic NAT pool exhausted for staff. | Rejected | Missing `overload` keyword in NAT source command (PAT). AI suggested adding more public IPs instead.
Responsible AI Audit Log: Override Analysis

## Slide 13
Apply AI: Analyze Customer Reviews
Completed: 10 Jun 2026
Certificate ID: 87fae7a2-55d8-475d-a39a-b52a5cda316c
Offered by IILM University through Cisco Networking Academy program.
Data Analytics Essentials
Completed: 11 Jun 2026
Certificate ID: d7eac08d-3bc6-4068-8894-2ef8a93c6024
Offered by IILM University through Cisco Networking Academy program.
Introduction to Modern AI
Completed: 11 Jun 2026
Certificate ID: a72f4179-688f-4f41-9c7b-5f91a4e2cf31
Offered by IILM University through Cisco Networking Academy program.
Completed Cisco Networking Academy Courses

## Slide 14
Deterministic Pre-Check Efficiency
• Syntax & State Validation: Regex rules in `rule_checker.py` detect shutdown ports, duplicate IPs, and timer mismatches instantly without API costs.
• Pre-Inference Filtering: Reduces LLM token usage and latency by filtering out 33.3% of routine Layer 1-3 configuration mistakes.
Mandatory Human Oversight
• No Unassisted CLI Pushes: Zero CLI commands are executed automatically on production nodes without engineer sign-off.
• Auditability: Every override action is permanently recorded in the audit log, creating a feedback loop for prompt refinements.
Responsible AI Safety & Guardrails

## Slide 15
Project Deliverables
• 30 multi-layer Cisco Packet Tracer lab cases with verified ground truth.
• Python `rule_checker.py` script for deterministic CLI pattern matching.
• Few-shot prompt engineering templates enforcing strict JSON schema.
• Executive Excel dashboard & Responsible AI audit log.
Academic & Industry Impact
• Fulfilled all requirements for B.Tech (CSE) degree at IILM University.
• Achieved an 83.3% diagnostic agreement rate across complex network topologies.
• Established a safe framework combining deterministic rules, LLM reasoning, and human safety oversight.
Key Outcomes & Value Addition

## Slide 16
Thank You!
NetSage AI: AI Deployment Automation for Cisco Network Troubleshooting
Mohammad Amaan Aslam
Roll No: 2410030089
IILM University, Greater Noida

## Slide 17
https://www.cisco.com/c/dam/en/us/products/collateral/routers/5400-enterprise-network-compute-system/datasheet-c78-738512.docx/_jcr_content/renditions/datasheet-c78-738512_1.png
Source: www.cisco.com
https://ipcisco.com/wp-content/uploads/2020/04/Network-Topology-Architectures.jpg
Source: ipcisco.com
Image Sources